## Slide 1: Low Precision Computation on Neural Networks (Week 11)
May 26, 2020
Sungjoo Yoo
Computing Memory Architecture Lab.
CSE, SNU
http://cmalab.snu.ac.kr

## Slide 2: Weekly Schedule
W1 17 Application (deep learning on FPGA)/SW app (MNIST/CIFAR)
W2 25 Verilog 1 Basics/Vivado tutorial (verification level of HW design)
W3 31 Verilog 2 Combinational circuits (Video pre-view homework + TA Q&A)/Simple adder using dsp (V+V, Verilog intro)
W4 4/7 Verilog 3 Sequential circuits/V*V processing element (PE) design 1
W5 14 Verilog 4 Design example & synthesizable code/V*V processing element (PE) design 2
W6 21 Convolution lowering and matrix multiplication accelerator/Convolution lowering (V0)
W7 28 Intro to Zynq & MV accelerator design/Zynq FPGA & synthesis, continue VV design & start MV accelerator design
W8 5/5 (Children’s day) Optional lab session is provided in lecture and lab hour
W9 12 Main memory (physical & virtual)/OS+FPGA (HOST~DEVICE) communication & MV design 2
W10 19 Bus and DMA (Video pre-view + TA Q&A)/custom IP & MV design 3
W11 26 Advanced deep learning #1 quantization for low precision computation/V0+DMA+8b
W12 6/2 Advanced deep learning #2 zero skipping/V0+DMA+8b+zero-skipping 1
W13 9 Final exam/V0+DMA+8b+zero-skipping 2
W14 16 Term project (V0+DMA+8b+zero) submission
Notes: From this we will start to work on the baseline MV accelerator.

## Slide 3: Notice
Final exam is scheduled on June 9th
Previous mid/final exams will be provided at eTL by June 2nd

## Slide 4: Agenda
Lecture
  Quantization for low precision computation on neural networks
Introduction to the lab on Week 11
  MV accelerator for 8-bit quantization

## Slide 5: Introduction
What is quantization?
  Reducing bit width of weight and activation (=feature map data), e.g., from 16-bit to 4-bit
weight
activation
MUL
ADD
Conventional convolution with 16bit data
Convolution with narrow (4bit) data
weight
activation
*
ADD
16b
16b
4b
4b
4b
4b
4b
4b
4b
4b
*
*
*

## Slide 6: Introduction (Cont’d): Quantization Trend
NVIDIA
  P40 and P4 support int8, i.e., 8-bit integer for inference purposes
[https://devblogs.nvidia.com/parallelforall/mixed-precision-programming-cuda-8/]

## Slide 7: SIMD or Vector (Addition)
A[0]
vector A
vector B
vector C
A[1]
A[2]
A[3]
B[0]
B[1]
B[2]
B[3]
C[0]
C[1]
C[2]
C[3]
+
+
+
+

## Slide 8
[Migacz, 2017]

## Slide 10: 32 and 16 bit Floating Point Representations

## Slide 11: Precision in Nvidia A100
[https://www.nvidia.com/content/dam/en-zz/Solutions/Data-Center/nvidia-ampere-architecture-whitepaper.pdf]

## Slide 12: Quantization for Low Precision: Agenda
Google’s int8 quantization
  Quantization and Training of Neural Networks for Efficient Integer-Arithmetic-Only Inference, CVPR 2018
NVIDIA’s int8 quantization
  8-bit Inference with TensorRT
Logarithm-based quantization
  Convolutional Neural Networks using Logarithmic Data Representation, CVPR 2017
Binary-weight neural network
  XNOR-Net: ImageNet Classification Using Binary Convolutional Neural Networks

## Slide 13: Google’s Int8 Solution
Goal: running int8 neural networks on CPUs supporting int8 SIMD instructions
Conversion, i.e., quantization from floating to 8-bit unsigned integer
q = round(r / S) + Z
r = S (q - Z)
-3.14
6.57
0
255
Z
Real value r
32-bit floating
Quantized value q
8-bit unsigned integer with 256 levels
[Jacob, 2018]

## Slide 14: Quantization Example
Calculating scale (S) and zero (Z) for int8
Example: 10.5  round(10.5/0.38)+83=28+83=111
q = round(r / S) + Z
r = S (q - Z)
-31.4
65.7
0
255
83
Real value r
32-bit floating
Quantized value q
8-bit unsigned int
-31.4  0 -31.4 = S*(0 – Z) SZ=31.4 Z=round(31.4/0.38)=83
65.7  255 65.7 = S*(255 –Z) 65.7+31.4=255S S=97.1/255=0.38
0
10.5
111
[Jacob, 2018]
29

## Slide 15: Integer Only Computation
Matrix multiplication, r3 = r1*r2
  Weight matrix r1 and activation matrix r2
[Jacob, 2018]
What if Z1 and Z2 are zero?

## Slide 16: Quantization Example: Zero Matching Case as a Trade-off Between Computation Cost and Accuracy
Calculating scale (S) and zero (Z) for int8
Example: 10.5  ceil(10.5 / 0.52)=21
Example: -31.4  -60
q = ceil(r / S)
r = Sq
-31.4
65.7
-127
127
0
Real value r
32-bit floating
Quantized value q
8-bit unsigned int
S = max (31.4/127, 65.7/127) = 0.52
0
10.5
21
[Jacob, 2018]
21
-60
Unused
value
Unused value range (& larger scale)
less precision

## Slide 17: Quantization Flow
Given a trained network, for each layer (separately)
Determine value ranges for weights and activations
  Weight: [min,max]
  Activation: exponential moving average (EMA) obtained in training
Re-train the network while applying quantization
  Forward pass: insert fake quantization while performing floating point (fp) comp.
    Fake quantization for weights: before each batch, quantize weights and use them in fp
    Fake quantization for activations: quantize layer output at each layer and use them in fp
  Backward pass: no change
Insert quantization into the network
  Weight: constant integer values
  Activation: quantization function, q = ceil(r / S) + Z is inserted into the network to covert layer output r to integer q during runtime
[Jacob, 2018]

## Slide 18: Quantization for Low Precision: Agenda
Google’s int8 quantization
  Quantization and Training of Neural Networks for Efficient Integer-Arithmetic-Only Inference, CVPR 2018
NVIDIA’s int8 quantization
  8-bit Inference with TensorRT
Logarithm-based quantization
  Convolutional Neural Networks using Logarithmic Data Representation, CVPR 2017
Binary-weight neural network
  XNOR-Net: ImageNet Classification Using Binary Convolutional Neural Networks

## Slide 20: Quantization for int8 in NVIDIA TensorRT
Examples of the distributions of activation
[Migacz, 2017]

## Slide 21: Quantization for int8 in NVIDIA TensorRT
Basic idea of determining the threshold
  Minimize information loss in the distribution of quantized data
  KL divergence is used as the metric of information loss
[Migacz, 2017]

## Slide 22: Kullback-Leibler (KL) Divergence
A measure of how one probability distribution diverges from a second expected probability distribution
The amount of information lost when Q is used to approximate P
The more similar distributions, the smaller KL divergence
[https://en.wikipedia.org/wiki/Kullback–Leibler_divergence]

## Slide 23: Quantization for int8 in NVIDIA TensorRT
Quantization examples
[Migacz, 2017]

## Slide 24: Quantization for int8 in NVIDIA TensorRT
[Migacz, 2017]

## Slide 25: Quantization for Low Precision: Agenda
Google’s int8 quantization
  Quantization and Training of Neural Networks for Efficient Integer-Arithmetic-Only Inference, CVPR 2018
NVIDIA’s int8 quantization
  8-bit Inference with TensorRT
Logarithm-based quantization
  Convolutional Neural Networks using Logarithmic Data Representation, CVPR 2017
Binary-weight neural network
  XNOR-Net: ImageNet Classification Using Binary Convolutional Neural Networks

## Slide 26: Logarithm-based Quantization (LogQuant)
Motivation
Less quantization errors for small values
No need of multiplication
  b1101 x b0100 = shift(b1101, 2)
  Multiplication becomes a shift operation
[Miyashita, 2016]

## Slide 27: Logarithm-based Quantization (LogQuant)
5.5 * 4.5 = b101.1 * b100.1
~ b101.1 * b100.0 = Bitshift(b101.1, 2)
= b10110 (22 in decimal)
= b10000 (leftmost ‘1’)
24.75 ~ 5.5*4=22 (error = 2.75)
After activation quantization (truncation case)
22  16 (b10000)

## Slide 28: LogQuant for Weight (5b) and Activation (4b)
Activations are in 4b log
LogQuant applied to weights of convolutional layers
1.7% (AlexNet) and 0.5% (VGG) loss
  Better than linear quantization
Conv weights are sensitive
Smaller base, 21/2 or 21/4 works well

## Slide 29: Quantization for Low Precision: Agenda
Google’s int8 quantization
  Quantization and Training of Neural Networks for Efficient Integer-Arithmetic-Only Inference, CVPR 2018
NVIDIA’s int8 quantization
  8-bit Inference with TensorRT
Logarithm-based quantization
  Convolutional Neural Networks using Logarithmic Data Representation, CVPR 2017
Binary-weight neural network
  XNOR-Net: ImageNet Classification Using Binary Convolutional Neural Networks

## Slide 30: XNOR-Net
Two types of network
  Binary-Weight network: only weights are binary, activations are 32-bit floating point values. It does not hurt accuracy while reducing weight size significantly
  XNOR-Net: both weight and activation are binary

## Slide 31: Binary-Weight-Network
x a
B
W
For k-th filter (output feature map) on l-th layer

## Slide 32: How to Obtain B and a ?
Solve this
c

## Slide 33: How to Obtain B and a ?
Solve this
*

## Slide 34: Training for Binary-Weight-Network
32bit
Forward pass with binary weights
Backward pass with binary weights
Update full-precision weights

## Slide 35: AlexNet Result
17% better than BinaryConnect (BC)

## Slide 36: ResNet and GoogLeNet
Binary weight: 8.5% and 5.8% loss (top1)
XNOR: 18.1% loss in ResNet
Deeper models require more bits
How many bits are required for GoogLeNet to have less than 1% accuracy loss?
  5~6 bits [Park, CVPR 2017]

## Slide 37: MV Accelerator
X
X
w11
w12
w21
w22
w11
w12
w21
w22
w11
w12
w21
w22
v1
v2
MAC1
MAC2
v1
v2
r1
r2
p1
p2
CPU
Memory (BRAM)
MV accelerator
r1
r2
Matrix M (N x N)
Input vector V
Result R
Buffer1
Register
Total execution cycles of MV = ((N/T)*(C+T+T))*(N/T)
TxT tile
C cycles
1
1
1
X
=
Buffer2
Time
C cycles
T
T
Tile 1
Tile 2
Tile N/T

## Slide 38: 8-bit MV Accelerator Reduces Communication and Reduces Area w.r.t. 32-bit One
X
X
w11
w12
w21
w22
w11
w12
w21
w22
v1
v2
MAC1
MAC2
v1
v2
r1
r2
p1
p2
CPU
Memory (BRAM)
MV accelerator
r1
r2
Matrix M (N x N)
Input vector V
Result R
Buffer1
Register
Total execution cycles of MV = ((N/T)*(C+T+T))*(N/T)
TxT tile
C’ cycles
1
1
1
X
=
Time
C’ cycles
T
T
Tile 1
Tile 2
Tile N/T
w11
w12
w21
w22
Buffer2

## Slide 39: Agenda
Lecture
  Quantization for low precision computation on neural networks
Introduction to the lab on Week 11
  MV accelerator for 8-bit quantization

## Slide 40: Appendix

## Slide 41: Fractional Exponent and Truncation in LogQuant
Baseexponent
  102, 23, 21/2, …
Fractional exponent (a.k.a radical or rational exponent) is often used in LogQuant
How to represent 21/2-base number?
  2.5 in decimal (10-base) number = 2*100 + 5*10-1
  2.5 in binary (2-base) number = 1*21 + 0*20 + 1*2-1 = 10.1
  2.5 in 21/2-base number = 1*(21/2)2+0*(21/2)1+0*(21/2)0+0*(2-1/2)1+1*(2-1/2)2 = 100.01
How to perform quantization?
  When truncation is adopted, only leading ‘1’ remains.
  2.5 = 100.01 (base 21/2)  100.00 (after quantization)

## Slide 42: Binary-Weight-Network Example
x 2
B
W
Assume a=2,
I*W ~ I*Bx2 =
(0.11x1-0.21x(-1) … -0.34x1+
-0.25x(-1)+0.61x1+…0.52x1)x2
Only additions and subtractions!