## Slide 1: Hardware System Design (Week 5) Verilog Design 4
April 14, 2020
Sungjoo Yoo
Computing Memory Architecture Lab.
CSE, SNU
http://cmalab.snu.ac.kr

## Slide 2: Weekly Schedule
W1 17 Application (deep learning on FPGA)/SW app (MNIST/CIFAR)
W2 25 Verilog 1 Basics/Vivado tutorial (verification level of HW design)
W3 31 Verilog 2 Combinational circuits (Video pre-view homework + TA Q&A)/Simple adder using dsp (V+V, Verilog intro)
W4 4/7 Verilog 3 Sequential circuits/V*V processing element (PE) design 1
W5 14 Verilog 4 Design example & synthesizable code/V*V processing element (PE) design 2
W6 21 Intro to Zynq & MV accelerator design/Zynq FPGA & synthesis, continue VV design & start MV accelerator design
W7 28 Mid-term exam cancelled. Main memory (physical & virtual)/OS+FPGA (HOST~DEVICE) communication & MV design 2
W8 5/5 (Children’s day) Optional lab session is provided in lecture and lab hour
W9 12 Bus and DMA (Video pre-view + TA Q&A)/custom IP & MV design 3
W10 19 Convolution lowering and matrix multiplication accelerator/Convolution lowering (V0)
W11 26 Advanced deep learning #1 quantization for low precision computation/V0+DMA+8b
W12 6/2 Advanced deep learning #2 zero skipping/V0+DMA+8b+zero-skipping 1
W13 9 Lecture summary/V0+DMA+8b+zero-skipping 2
W14 16 Final exam/Term project (V0+DMA+8b+zero) submission
Notes: In our schedule, we design the hardware accelerator for four weeks as the blue part shows.

## Slide 3: Agenda
Lecture
  PE controller overview
  Synthesizable Verilog code
  Logic optimization review
Introduction to the lab on Week 5
  Designing the PE controller

## Slide 4: Final Project Overview: Matrix Multiplication IP
MY_IP
Processing Element (PE)
Float32 MUL+ACC
[32:0] REG[0:127] (BRAM inference)
ADDR
DIN
DOUT
CTRL
TRUE DP
BRAM
C
B
A
DOUT
ADDR
FSM
[32:0] REG[0:127] (BRAM inference)
BRAM
INTERFACE
Shift(16)
PS
AXI_SLAVE INTERFACE
OUT
OUT
DIN
COUNTER
2-cyc
RESET
W5 (pe_controller)
W4 (pe)
W2~W3

## Slide 5: Processing Element (PE) for Dot Product (V*V)
Two step operations for dot product
Step 1
  Testbench writes the data of weight matrix to the internal memory (peram) via ‘addr’ and ‘din’.
  64 32bit data are written
Step 2
  Testbench writes 64 data of vector via ‘ain’ and ‘addr’
  After that, PE provides the output via ‘dout’
peram
MAC
addr
din
valid
ain
dout
dvalid
we
6b
32b
32b
32b
32b
Testbench
my_pe
Matrix (M)
Vector (V)
Notes: The figure on the left shows the basic structure of processing element.
The multi-bit signals are shown in bold and thick arrows.
As explained on the right of this slide,
There are two execution steps in the PE.
In step 1, we write data (in fact, the elements of matrix in matrix-vector multiplication) to the internal memory, i.e., peram[]. For this operation we set ‘we’ to ‘1’.
In step 2, we do computation where the MAC unit takes three inputs, one from peram[], another from the input port ain, and the other from its own output (for accumulation). For this operation, we set ‘we’ to ‘0’.
Let’s see how each step works in the following slides.

## Slide 6: PE Controller in Week 5
PE controller enables PE to perform two-step operations for dot product
Step 1
  Testbench writes the data of weight matrix to the internal memory (peram) via ‘addr’ and ‘din’.
  64 32bit data are written
Step 2
  Testbench writes 64 data of vector via ‘ain’ and ‘addr’
  After that, PE provides the output via ‘dout’
addr
din
valid
ain
dout
dvalid
we
pe_controller
my_pe
Matrix (M)
Vector (V)
start
done
aclk
areset_n
raddr
rddata
wrdata
Control
function, memory
& connection
Notes: The figure on the left shows the basic structure of processing element.
The multi-bit signals are shown in bold and thick arrows.
As explained on the right of this slide,
There are two execution steps in the PE.
In step 1, we write data (in fact, the elements of matrix in matrix-vector multiplication) to the internal memory, i.e., peram[]. For this operation we set ‘we’ to ‘1’.
In step 2, we do computation where the MAC unit takes three inputs, one from peram[], another from the input port ain, and the other from its own output (for accumulation). For this operation, we set ‘we’ to ‘0’.
Let’s see how each step works in the following slides.

## Slide 7: PE Controller
PE controller consists of PE, FSM and global BRAM
PE controller takes 32 inputs (data[0]~data[31]) from testbench
  PE controller writes the former 16 data (data[0]~data[15]) on local register (peram) in PE, and the latter 16 data (data[16]~data[31]) on global BRAM on PE controller
FSM controls PE to calculate inner product (e.g., data[0]*data[16] + data[1]*data[17]+ … + data[15]*data[31]) with several states
Matrix (M)
Vector (V)
peram
MAC
6b
32b
32b
32b
32b
globalmem
Testbench
PE
16 data
16 data
16 data
PE controller
FSM

## Slide 8: States in FSM
S_IDLE:
  Idle state. Starts operation with state transition to S_LOAD, when input ‘start==1’.
S_LOAD:
  Loads 16 data into local memory in PE and load 16 data into global BRAM. After data loading, state moves to S_CALC.
S_CALC:
  Calculate “inner product” with 16 data from local memory of PE, 16 data from global memory. After calculation, state moves to S_DONE.
S_DONE:
  Gives ‘done’ as 1. After 5 cycles, state moves to S_IDLE

## Slide 9: Idle state
peram
MAC
6b
32b
32b
32b
32b
globalmem
Testbench
PE
PE controller
start
done
aclk
areset_n
raddr
rddata
wrdata
Matrix (M)
Vector (V)

## Slide 10: Load state
peram
MAC
6b
32b
32b
32b
32b
globalmem
Testbench
PE
PE controller
start
done
aclk
areset_n
raddr
rddata
wrdata
16 data
Matrix (M)
Vector (V)

## Slide 11: Processing Element (PE): Step 1
peram
MAC
addr
din
valid
ain
dout
dvalid
we
6b
32b
32b
32b
32b
‘1’
Control
logic
Step 1
  Testbench writes the data of weight matrix to the internal memory (peram) via ‘addr’ and ‘din’.
  64 32bit data (matrix elements) are written
  Write enable, we = ‘1’
my_pe
Matrix (M)
Vector (V)
Notes: In step 1, we write matrix elements to the local register, peram.
To do that, we set ‘we’ to ‘1’.
We also set addr and din to write data to peram.
peram has 64 elements. Thus, we will perform write operations 64 times while incrementing ‘addr’ and providing new data to ‘din’.

## Slide 12: Load state
peram
MAC
6b
32b
32b
32b
32b
globalmem
Testbench
PE
PE controller
start
done
aclk
areset_n
raddr
rddata
wrdata
16 data
Matrix (M)
Vector (V)

## Slide 13: Calc state
peram
MAC
6b
32b
32b
32b
32b
globalmem
Testbench
PE
16 data
PE controller
start
done
aclk
areset_n
raddr
rddata
wrdata
16 data
Matrix (M)
Vector (V)

## Slide 14: Processing Element (PE): Step 2
peram
MAC
addr
din
valid
ain
dout
dvalid
we
6b
32b
32b
32b
32b
Control
logic
‘0’
‘1’
Step 2
  Testbench writes 64 data of vector via ‘ain’ and ‘addr’
  valid = ‘1’, we = ‘0’
my_pe
a
b
c
d
1
2
3
4
Matrix (M)
Vector (V)
Notes: In Step 2, we perform computation, i.e., the MAC performs dot-product operation between a set of matrix elements (in peram) and a set of vector elements provided to ‘ain’.
The testbench (later, our accelerator design which instantiates PEs) will provide 64 vector elements via ‘ain’.
First, we (=the testbench) need to set ‘we’ to ‘0’ and ‘valid’ to ‘1’ as the slide shows.
Then, the testbench needs to provide 64 data via ‘ain’ while incrementing ‘addr’.
In Step 2, for each ‘addr’, peram provides the associated data, e.g., if addr = 10, peram[10] is provided to MAC.

## Slide 15: Processing Element (PE): Step 2
peram
MAC
addr
din
valid
ain
dout
dvalid
we
6b
32b
32b
32b
32b
‘0’
‘1’
Step 2
  Testbench writes 64 data of vector via ‘ain’ and ‘addr’
  In cycle 1, the first input pair of matrix and vector elements, a and 1 is provided to the MAC unit
my_pe
a
b
c
d
1
2
3
4
Matrix (M)
Vector (V)
1
a
Control
logic
Notes: In Step 2, we perform computation, i.e., the MAC performs dot-product operation between a set of matrix elements (in peram) and a set of vector elements provided to ‘ain’.
The testbench (later, our accelerator design which instantiates PEs) will provide 64 vector elements via ‘ain’.
First, we (=the testbench) need to set ‘we’ to ‘0’ and ‘valid’ to ‘1’ as the slide shows.
Then, the testbench needs to provide 64 data via ‘ain’ while incrementing ‘addr’.
In Step 2, for each ‘addr’, peram provides the associated data, e.g., if addr = 10, peram[10] is provided to MAC.

## Slide 16: Processing Element (PE): Step 2
peram
MAC
addr
din
valid
ain
dout
dvalid
we
6b
32b
32b
32b
32b
‘0’
‘1’
Step 2
  Testbench writes 64 data of vector via ‘ain’ and ‘addr’
  In cycle 1, the first input pair of matrix and vector elements, a and 1 is provided to the MAC unit
  In cycle 2, 2nd input pair of b and 2 is provided. Note that the partial sum, Psum is also an input to the MAC unit and accumulated with the new product
my_pe
a
b
c
d
1
2
3
4
Matrix (M)
Vector (V)
2
b
Psum (=a*1)
Control
logic
Notes: In Step 2, we perform computation, i.e., the MAC performs dot-product operation between a set of matrix elements (in peram) and a set of vector elements provided to ‘ain’.
The testbench (later, our accelerator design which instantiates PEs) will provide 64 vector elements via ‘ain’.
First, we (=the testbench) need to set ‘we’ to ‘0’ and ‘valid’ to ‘1’ as the slide shows.
Then, the testbench needs to provide 64 data via ‘ain’ while incrementing ‘addr’.
In Step 2, for each ‘addr’, peram provides the associated data, e.g., if addr = 10, peram[10] is provided to MAC.

## Slide 17: Processing Element (PE): Step 2
peram
MAC
addr
din
valid
ain
dout
dvalid
we
6b
32b
32b
32b
32b
‘0’
‘1’
Step 2
  Testbench writes 64 data of vector via ‘ain’ and ‘addr’
  In cycle 1, the first input pair of matrix and vector elements, a and 1 is provided to the MAC unit
  In cycle 2, 2nd input pair of b and 2 is provided. Note that the partial sum, Psum is also an input to the MAC unit and accumulated with the new product
  In cycle 3, 3rd input pair is provided and its product is accumulated to the previous partial sum
my_pe
a
b
c
d
1
2
3
4
Matrix (M)
Vector (V)
3
c
Psum (=a*1+b*2)
Control
logic
Notes: In Step 2, we perform computation, i.e., the MAC performs dot-product operation between a set of matrix elements (in peram) and a set of vector elements provided to ‘ain’.
The testbench (later, our accelerator design which instantiates PEs) will provide 64 vector elements via ‘ain’.
First, we (=the testbench) need to set ‘we’ to ‘0’ and ‘valid’ to ‘1’ as the slide shows.
Then, the testbench needs to provide 64 data via ‘ain’ while incrementing ‘addr’.
In Step 2, for each ‘addr’, peram provides the associated data, e.g., if addr = 10, peram[10] is provided to MAC.

## Slide 18: Done state
peram
MAC
6b
32b
32b
32b
32b
globalmem
Testbench
PE
PE controller
start
done
aclk
areset_n
raddr
rddata
wrdata
Matrix (M)
Vector (V)

## Slide 19: Processing Element (PE): Step 2
peram
MAC
addr
din
valid
ain
dout
dvalid
we
6b
32b
32b
32b
32b
‘1’
Step 2
  Testbench writes 64 data of vector via ‘ain’ and ‘addr’
  After finishing the dot product operation, PE provides the output via ‘dout’
my_pe
Psum (=a*1+b*2+c*3+d*4)
a
b
c
d
1
2
3
4
Matrix (M)
Vector (V)
Control
logic
1
Notes: After completing the dot-product operation between two vectors (one matrix row and the other input vector),
The MAC unit provides the output while setting ‘dvalid’ to ‘1’.

## Slide 20: Basic Logic Design With Verilog IV
- Design Examples and Synthesizable Code

## Slide 21: Example: Simple PE (Processing Element) Controller
IDLE
INIT
LOAD
CALC
init
counter<3
rst
counter<15
RES
counter<3
init’
Simple PE controller
  IDLE: PE waits for input data.
  INIT: When init is changed into 1. PE controller starts to get data from outside (din). Internal signal, ‘pe_en’, is changed into 1.
  LOAD: PE controller gets 4 data entries from outside (din) and gives it to PE for 4 cycles.
  CALC: PE computes output data for 16 cycles.
  RES: PE controller gets 4 data entries (result) from PE and gives it to outside (dout) for 4 cycles. State is turned into IDLE and ‘pe_en’ is changed into 0 when it finishes operation
PE
PE
controller
rst
init
din
dout
2 bit counter
clk
4 bit counter
init
Load
input
Calculation
Return
result
4 cycles
4 cycles
16 cycles
pe_en

## Slide 22: Example: Simple PE controller - continued
module pe_controller (clk, rst, init, din, dout);
input clk, rst, init;
input [31:0] din;
output [31:0] dout;
reg [1:0] present_state, next_state; // present state and next state
reg [3:0] count15; // register for counter
reg [1:0] count3;
reg counter_rst15;
reg counter_rst3;
reg pe_en; // enable for PE
parameter IDLE = 3'd0, INIT = 3'd1, LOAD = 3'd2, CALC = 3'd3, RES = 3'd4;
// PE
PE my_pe (
.clk(clk),
.rst(rst),
.en(pe_en),
.din(din),
.dout(dout)
);
// counter
always @(posedge clk or posedge counter_rst15)
if(counter_rst15) count15 <= 0;
else count15 <= count15+1;
always @(posedge clk or posedge counter_rst3)
if(counter_rst3) count3 <= 0;
else count3 <= count3+1;

## Slide 23: Example: Simple PE controller
// part 1: initialize to state IDLE and update present state register
always @(posedge clk or posedge rst)
if(rst) present_state <= IDLE; else present_state <= next_state;
// part 2: determine next state
always @(*)
case(present_state)
IDLE: if(init) next_state = INIT; else next_state = present_state;
INIT: next_state = LOAD;
LOAD: if(count3==3) next_state = CALC; else next_state = present_state;
CALC: if(count15==15) next_state = RES; else next_state = present_state;
RES: if(count3==3) next_state = IDLE; else next_state = present_state;
endcase
// part 3: evaluate output (in this case internal registers)
always @(*)
case (present_state)
CALC: counter_rst15 = 0; // counter for CALC continues to tick
default: counter_rst15 = 1;
endcase
always @(*)
case (present_state)
LOAD: counter_rst3 = 0; // counter for LOAD continues to tick
RES: counter_rst3 = 0; // counter for RES continues to tick
default: counter_rst3 = 1;
endcase
always @(*)
case (present_state)
IDLE: pe_en = 0;
default: pe_en = 1;
endcase
endmodule

## Slide 24: Example: Simple PE controller
IDLE
0
INIT
1
LOAD
2
CALC
3
init
counter<3
rst
counter<15
RES
4
counter<3
init’

## Slide 25: Logic Synthesizer
part 2
part 1
part 3

## Slide 26: Logic Synthesis Environment
Design environment
Design constraints
RTL code
Technology library

## Slide 27: Design Constraints
Include clock, input delay and output delay
  E.g., 100MHz, every input/output has 0.5ns delay
Clock signal specification
  Period : clock period
  Duty cycle : proportion of time during which a component is operated
  Transition time : rise time and fall time of the clock
  Skew : clock network delay
Delay specifications
  Maximum
  Minimum

## Slide 28: Flow in Synthesizer
Like a selection from IP catalog

## Slide 29: The Architecture of Synthesizer
Front end
  Parsing phase
    Check the syntax of the source code
    Create internal components
  Elaboration phase
    Connect the internal components
    Unroll loops & expand generate-loops
    Set up parameters passing for tasks and functions
 Complete description of the input circuit

## Slide 30: Writing Synthesizable Code
Synthesizable operators
Synthesizable constructs
  assignment statement
  if .. else statement
  case statement
  loop structures
  always statement
Memory synthesis approaches

## Slide 31: Synthesizable Operators
  Analysis/translation step extracts the logical functions from a language structure
  Operators with gray blocks are generally the exceptions for synthesis
  Operands can be wire net type, reg variable type and parameter, as well as functions

## Slide 32: Synthesizable if-else Statements
Usually synthesize into a 2-to-1 multiplexer
  Nested if-else  priority-encoded, cascaded combination of multiplexers
For combinational logic
  Completely specified?
always @(enable or data)
if (enable) y = data; //infer a latch
always @(enable or data)
if (enable) y = data;
else y = y; //infer a latch
always @(enable or data)
if (enable) y = data;
else y = x; //infer a mux

## Slide 33: Latch Inference --- Incomplete if-else Statements
// creating a latch
module latch_infer_if(enable, data, y);
input enable, data;
output reg y;
always @(enable or data)
if (enable) y = data; // infer a latch for y

## Slide 34: Synthesizable if-else Statements
For sequential logic
  Completely specified?
  Synthesis tool will remove the redundant expression
always @(posedge clk)
if (enable) y <= data;
else y <= y; // a redundant expression

## Slide 35: Coding Style
Avoid using any latches in a design
Assign outputs for all input conditions to avoid inferred latches
Two ways to avoid latch inference:
always @(enable or data)
y = 1’b0; // initialize y to its initial value.
if (enable) y = data;
always @(enable or data)
if (enable) y = data;
else y = x; // complete if-else statement

## Slide 36: Synthesizable case Statements
A case statement
  Infers a multiplexer
  Completely specified?

## Slide 37: Latch Inference --- Incomplete Case Statements
// Creating a latch
module latch_infer_case(select, data, y);
…
output reg y;
always @(select or data)
case (select)
2'b00: y = data[select];
2'b01: y = data[select];
2'b10: y = data[select];
// infer a latch
endcase

## Slide 38: Latch Inference --- Complete Case Statements
module mux(select, data, y);
…
output reg y;
always @(select or data)
case (select)
2'b00: y = data[select];
2'b01: y = data[select];
2'b10: y = data[select];
default: y = 2'b11; // mux
endcase

## Slide 39: Mixed Use of posedge/level Signals
// the mixed usage of posedge and level signals
// the result cannot be synthesized
module DFF_bad (clk, reset, d, q);
…
// the body of DFF
always @(posedge clk or reset)
begin
if (reset) q <= 1'b0;
else q <= d;
end
Error: Do not mix posedge/negedge use with plain(level) signal references

## Slide 40: Mixed Use of posedge/negedge Signals
// the mixed usage of posedge/negedge signal
module DFF_good (clk, reset_n, d, q);
…
// the body of DFF
always @(posedge clk or negedge reset_n)
begin
if (!reset_n) q <= 1'b0;
else q <= d;
end
*Not recommended

## Slide 41: Loop Structures
Loop statements for, while, and forever are synthesizable except that while and forever must contain timing control @(posedge clk) or @(negedge clk)
repeat is generally not synthesizable
// an N-bit adder using for loop.
module nbit_adder_for( x, y, c_in, sum, c_out);
parameter N = 4; // default size
…
integer i;
…
always @(x or y or c_in) begin
co = c_in;
for (i = 0; i < N; i = i + 1)
{co, sum[i]} = x[i] + y[i] + co; // At the elaboration phase, the always block is expanded into the following statements
c_out = co;
end

## Slide 42: Loop Structures - An Incorrectly Synthesizable Example
// a multiple cycle example --- This is an incorrect version.
…
parameter N = 8;
parameter M = 4;
input clk, reset_n;
…
integer i;
// what does the following statement do?
always @(posedge clk or negedge reset_n) begin
if (!reset_n) total <= 0;
else for (i = 0; i < M; i = i + 1)
if (data_a[i] == 1) total <= total + data_b;
end
Q: Why the synthesized result is like this? Due to the non-blocking statement!

## Slide 43: Loop Structures - An Incorrectly Synthesizable Example
// a multiple cycle example --- This is an incorrect version.
…
parameter N = 8;
parameter M = 4;
input clk, reset_n;
…
integer i;
// what does the following statement do?
always @(posedge clk or negedge reset_n) begin
if (!reset_n) total <= 0;
else begin
if (data_a[0] == 1) total <= total + data_b;
if (data_a[1] == 1) total <= total + data_b;
if (data_a[2] == 1) total <= total + data_b;
if (data_a[3] == 1) total <= total + data_b;
end
end

## Slide 44: Loop Structures - An Incorrectly Synthesizable Example

## Slide 45: Loop Structures - An Correctly Synthesizable Example
// a multiple cycle example --- This is an correct version.
…
parameter N = 8;
parameter M = 4;
input clk, reset_n;
…
integer i;
always @(*) begin
total = 0;
for (i = 0; i < M; i = i + 1)
if (data_a[i] == 1) total = total + data_b;
end

## Slide 46: The Architecture of Synthesizer
Back end
  Analysis/translation
    Include managing the design hierarchy
    Extract the FSM
    Explore resource sharing
  Logic synthesis (logic optimization)
    Create a new gate network computing the functions specified by a set of Boolean functions, one per primary output
    Balance a number of concerns : functional metric and non-functional metric (area, power, delay)
  Netlist generation

## Slide 47: Logic Optimization
FSM optimization in sequential circuit
  State minimization in FSM + input/output/state encoding + combinational circuit optimization
part 2
part 1
part 3
# states  # F/Fs

## Slide 48: Logic Optimization
Combinational circuit
  E.g., Minimum cover selection on K-map

## Slide 49: Algorithmic Approach to State Minimization
Goal – identify and combine states that have equivalent behavior
Equivalent States: Same output & Same transition
  Same output
  For all input combinations, states transition to same or equivalent states
Row Matching Method: Algorithm Sketch
  1. Place all states in one set
  2. Initially partition set based on output behavior
  3. Successively partition resulting subsets based on next state transitions
  4. Repeat (3) until no further partitioning is required
    states left in the same set are equivalent
  Polynomial time procedure

## Slide 50: State Minimization Example
Input Next State Output
Sequence Present State X=0 X=1 X=0 X=1
Reset S0 S1 S2 0 0
0 S1 S3 S4 0 0
1 S2 S5 S6 0 0
00 S3 S0 S0 0 0
01 S4 S0 S0 1 0
10 S5 S0 S0 0 0
11 S6 S0 S0 1 0
Sequence Detector for 010 or 110
S0
S3
S2
S1
S5
S6
S4
1/0
0/0
1/0
1/0
0/1
0/0
1/0
0/0
1/0
0/0
1/0
0/1
1/0
0/0

## Slide 51: Method of Successive Partitions
( S0 S1 S2 S3 S4 S5 S6 )
( S0 S1 S2 S3 S5 ) ( S4 S6 )
( S0 S3 S5 ) ( S1 S2 ) ( S4 S6 )
( S0 ) ( S3 S5 ) ( S1 S2 ) ( S4 S6 )
Input Next State Output
Sequence Present State X=0 X=1 X=0 X=1
Reset S0 S1 S2 0 0
0 S1 S3 S4 0 0
1 S2 S5 S6 0 0
00 S3 S0 S0 0 0
01 S4 S0 S0 1 0
10 S5 S0 S0 0 0
11 S6 S0 S0 1 0
A
B
A
A
A
B
A
A
A
B
A
A
A
A
A
A

## Slide 52: Method of Successive Partitions
( S0 S1 S2 S3 S4 S5 S6 )
( S0 S1 S2 S3 S5 ) ( S4 S6 )
( S0 S3 S5 ) ( S1 S2 ) ( S4 S6 )
( S0 ) ( S3 S5 ) ( S1 S2 ) ( S4 S6 )
Input Next State Output
Sequence Present State X=0 X=1 X=0 X=1
Reset S0 S1 S2 0 0
0 S1 S3 S4 0 0
1 S2 S5 S6 0 0
00 S3 S0 S0 0 0
01 S4 S0 S0 1 0
10 S5 S0 S0 0 0
11 S6 S0 S0 1 0
A
B
A
A
A
B
A
A
A
B
A
A
A
A
A
A

## Slide 53: Method of Successive Partitions
( S0 S1 S2 S3 S4 S5 S6 )
( S0 S1 S2 S3 S5 ) ( S4 S6 )
( S0 S3 S5 ) ( S1 S2 ) ( S4 S6 )
( S0 ) ( S3 S5 ) ( S1 S2 ) ( S4 S6 )
Input Next State Output
Sequence Present State X=0 X=1 X=0 X=1
Reset S0 S1 S2 0 0
0 S1 S3 S4 0 0
1 S2 S5 S6 0 0
00 S3 S0 S0 0 0
01 S4 S0 S0 1 0
10 S5 S0 S0 0 0
11 S6 S0 S0 1 0
A
B
A
A
A
B
A
A
A
B
A
A
A
A
A
A

## Slide 54: Method of Successive Partitions
( S0 S1 S2 S3 S4 S5 S6 )
( S0 S1 S2 S3 S5 ) ( S4 S6 )
( S0 S3 S5 ) ( S1 S2 ) ( S4 S6 )
( S0 ) ( S3 S5 ) ( S1 S2 ) ( S4 S6 )
Input Next State Output
Sequence Present State X=0 X=1 X=0 X=1
Reset S0 S1 S2 0 0
0 S1 S3 S4 0 0
1 S2 S5 S6 0 0
00 S3 S0 S0 0 0
01 S4 S0 S0 1 0
10 S5 S0 S0 0 0
11 S6 S0 S0 1 0
C
D
E
C
C
C
C
C
C
C
C
C
C
D
D
E
E

## Slide 55: Method of Successive Partitions
( S0 S1 S2 S3 S4 S5 S6 )
( S0 S1 S2 S3 S5 ) ( S4 S6 )
( S0 S3 S5 ) ( S1 S2 ) ( S4 S6 )
( S0 ) ( S3 S5 ) ( S1 S2 ) ( S4 S6 )
Input Next State Output
Sequence Present State X=0 X=1 X=0 X=1
Reset S0 S1 S2 0 0
0 S1 S3 S4 0 0
1 S2 S5 S6 0 0
00 S3 S0 S0 0 0
01 S4 S0 S0 1 0
10 S5 S0 S0 0 0
11 S6 S0 S0 1 0
C
D
E
C
C
C
C
C
C
C
C
C
C
D
D
E
E

## Slide 56: Method of Successive Partitions
( S0 S1 S2 S3 S4 S5 S6 )
( S0 S1 S2 S3 S5 ) ( S4 S6 )
( S0 S3 S5 ) ( S1 S2 ) ( S4 S6 )
( S0 ) ( S3 S5 ) ( S1 S2 ) ( S4 S6 )
Input Next State Output
Sequence Present State X=0 X=1 X=0 X=1
Reset S0 S1 S2 0 0
0 S1 S3 S4 0 0
1 S2 S5 S6 0 0
00 S3 S0 S0 0 0
01 S4 S0 S0 1 0
10 S5 S0 S0 0 0
11 S6 S0 S0 1 0
S1 is equivalent to S2
S3 is equivalent to S5
S4 is equivalent to S6
C
D
E
C
C
C
C
C
C
C
C
C
C
D
D
E
E

## Slide 57: Minimized FSM
Input Next State Output
Sequence Present State X=0 X=1 X=0 X=1
Reset S0 S1' S1' 0 0
0 + 1 S1' S3' S4' 0 0
X0 S3' S0 S0 0 0
X1 S4' S0 S0 1 0
State minimized sequence detector for 010 or 110
S0
S1’
S3’
S4’
X/0
1/0
1/0
0/1
0/0
X/0
S0
S3
S2
S1
S5
S6
S4
1/0
0/0
1/0
1/0
0/1
0/0
1/0
0/0
1/0
0/0
1/0
0/1
1/0
0/0
( S0 ) ( S3 S5 ) ( S1 S2 ) ( S4 S6 )

## Slide 58: Minimized FSM
Input Next State Output
Sequence Present State X=0 X=1 X=0 X=1
Reset S0 S1' S1' 0 0
0 + 1 S1' S3' S4' 0 0
X0 S3' S0 S0 0 0
X1 S4' S0 S0 1 0
State minimized sequence detector for 010 or 110
S0
S1’
S3’
S4’
X/0
1/0
1/0
0/1
0/0
X/0
S0
S3
S2
S1
S5
S6
S4
1/0
0/0
1/0
1/0
0/1
0/0
1/0
0/0
1/0
0/0
1/0
0/1
1/0
0/0
( S0 ) ( S3 S5 ) ( S1 S2 ) ( S4 S6 )

## Slide 59: Minimized FSM: A Simple Illustration
State minimized sequence detector for 010 or 110
Input Next State Output
Sequence Present State X=0 X=1 X=0 X=1
Reset S0 S1' S1' 0 0
0 + 1 S1' S3' S4' 0 0
X0 S3' S0 S0 0 0
X1 S4' S0 S0 1 0
S0
S1’
S3’
S4’
X/0
1/0
1/0
0/1
0/0
X/0
S0
S2
S1
1/0
0/0
1/0
0/0
1/0
0/0
S3’
S4’
1/0
0/1
X/0
( S0 ) ( S3 S5 ) ( S1 S2 ) ( S4 S6 )

## Slide 60: Minimized FSM
State minimized sequence detector for 010 or 110
Input Next State Output
Sequence Present State X=0 X=1 X=0 X=1
Reset S0 S1' S1' 0 0
0 + 1 S1' S3' S4' 0 0
X0 S3' S0 S0 0 0
X1 S4' S0 S0 1 0
S0
S1’
S3’
S4’
X/0
1/0
1/0
0/1
0/0
X/0
S0
S3
S2
S1
S5
S6
S4
1/0
0/0
1/0
1/0
0/1
0/0
1/0
0/0
1/0
0/0
1/0
0/1
1/0
0/0
State
Minimization!

## Slide 61: The Architecture of Synthesizer
Back end
  Analysis/translation
    Include managing the design hierarchy
    Extract the FSM
    Explore resource sharing
  Logic synthesis (logic optimization)
    Create a new gate network computing the functions specified by a set of Boolean functions, one per primary output
    Balance a number of concerns : functional metric and non-functional metric (area, power, delay)
  Netlist generation

## Slide 62: Agenda
Lecture
  PE controller overview
  Synthesizable Verilog code
  Logic optimization review
Introduction to the lab on Week 5
  Designing the PE controller